## Slide 1: Layered Interval Codes for TCAM-based Classification
David Hay, Politecnico di Torino
Joint work with Anat Bremler-Barr (IDC), Danny Hendler (BGU) and Boris Farber (IDC)
This work is supported by a Cisco grant

## Slide 2: Outline
Packet Classification and TCAM devices
The range rule representation problem
Our solution: Layered Interval Code
Conclusions

## Slide 3: Packet Classification
Action
----
----
----
----
----
----
Rule
Action
Policy Database (classifier)
Packet Classification
Forwarding Engine
Incoming Packet
HEADER

## Slide 4: Multi-field Packet Classification
Given a database with N rules, find the action associated with the highest priority rule matching an incoming packet
Example: A packet (152.168.3.32, 152.163.171.71, …, TCP) would have action A2 applied to it

## Slide 5: Applications
Address Lookup
  Where to send an incoming packet?
  Usually needs only destination IP address
Firewall, ACL, Intrusion Detection Schemes
  Which packet to accept or deny?
  Usually needs 5 fields: source-address, dest-address, source-port, dest-port, protocol
Packet classification lies in the critical path of the
packet, and should be performed at very high rate
(~125 million packets per second for 40 Gb/s network)

## Slide 6: Software Solutions
Many exist in the literature:
  Linear Search
  Tree-based (e.g. Trie, Grid of Tries…)
  Cross-producting
  HiCuts
  Bloom-Filter Based Data Structures
  …
All software solutions introduce non-constant
classification time (and we usually have only 1
cycle)

## Slide 7: Towards a Hardware Solution
Rules in the policy database can be written in a ternary alphabet, using 0,1,
In the 5-field IPv4 rules (for firewall, ACL…), we can represent each rule as a string of 104 ternary symbols
100110001010100000000011

## Slide 8: Packet Classification w/ TCAM
Encoder
Match lines
5-Field Packet Header (Search Key)
0
1
2
3
4
6
5
7
8
9
2
0
1
2
3
4
6
5
7
8
9
accept
accept
accept
deny
deny
deny
deny
deny
deny
accept
TCAM Array
Each entry is a word in {0,1,}W and represents a rule
Notes: Why Packet Classification in IP; first match; Any router/firewall. Alternative data structures in software (list, tree, trie). No deterministic latency.
Example

## Slide 9: Example
Encoder
Match lines
0
1
2
3
4
6
5
7
8
9
deny
log
accept
deny
deny
deny
deny
limit
deny
accept
00111011010100001001111
1100000011100101000110
100101000010001101001000
001110
11100100100101010100
11100100100101001

001110
10101010
111111111111111111111111
0011101010101001110001110001110
0
0
0
1
0
1
0
1
0
1
3

## Slide 10: TCAM Benefits and Disadvantages
Deterministic Search Throughput—O(1) search
  Extremely important
  The only real solution that can do that
However, relatively costly and power consuming
  150$ for small (4Mbit) TCAM
~10 millions TCAM devices already deployed
Notes: Free extra symbol is picture

## Slide 11: Typical Dimensions and Speed
100K-200K rules
100-150 symbols per rule
Deterministic Search Throughput—O(1) search
133 million searches per second for 144-bit keys
  Suitable even for 40 Gb/s IPv4 traffic
Few dozens (~40) extra symbols are left in each entry, that can be used to optimize TCAM performance

## Slide 12: Outline
Packet Classification and TCAM devices
The range rule representation problem
Our solution: Layered Interval Code
Conclusions

## Slide 13: Range Rules
Rule | Source address | Source port | Dest-address | Dest-port | Protocol | Action
Rule 1 | 123.25.0.0/16 | 80 | 255.2.3.4/32 | 80 | TCP | Accept
Rule 2 | 13.24.35.0/24 | >1023 | 255.2.127.4/31 | 5556 | TCP | Deny
Rule 3 | 16.32.223.14 | 20-50 | 255.2.3.4/31 | 50-70 | UDP | Accept
Rule 4 | 22.2.3.4 | 1-6 | 255.2.3.0/21 | 20-22 | TCP | Limit
Rule 5 | 255.2.3.4 | 12-809 | 255.2.3.4 | 17-190 | ICMP | Log
Range rule = rule that contains range field
  Usually source-port or dest-port
  E.g., all packets with dest-port [1024,216-1] are denied

## Slide 14: Range Rules Representation
Some ranges are easy to represent
  [20, 23] = {10100,10101,10110,10111} = 101
But what about [1,6]?

## Slide 15: Prefix Expansion
Use multiple entries to code a single rule
[1,6]= {001, 01,10, 110} – 4 entries
Every rule that contains [1,6] needs 4 entries
  Maximum expansion 2W-2 for range [1,2W-2] (W is the field width)
[Srinivasan, Varghese, Suri, Waldvogel; 1998]
Rule | Source address | Source port | Destination address | Destination port | Protocol | Action
Rule 1 | 123.25.0.0/16 | 80 | 255.2.3.4/32 | 80 | TCP | Accept
Rule 2 | 13.24.35.0/24 | >1023 | 255.2.127.4/31 | 5556 | TCP | Deny
Rule 3 | 16.32.223.14 | 20-50 | 255.2.3.4/31 | 50-70 | UDP | Accept
Rule 4.1 | 22.2.3.4 | 1 | 255.2.3.0/21 | 20-22 | TCP | Limit
Rule 4.2 | 22.2.3.4 | 2-3 | 255.2.3.0/21 | 20-22 | TCP | Limit
Rule 4.3 | 22.2.3.4 | 4-5 | 255.2.3.0/21 | 20-22 | TCP | Limit
Rule 4.4 | 22.2.3.4 | 6 | 255.2.3.0/21 | 20-22 | TCP | Limit
Rule 5 | 255.2.3.4 | 12-809 | 255.2.3.4 | 17-190 | ICMP | Log
Notes: Illustrate two range fields

## Slide 16: Prefix Expansion
For rules with two range fields, we need the Cartesian product of the expansion
In real TCAMs cause 6 times more entries!
  More power, more memory, more potential errors
Active research to reduce this cost: [Liu], [van-Lunteren, Engbersen], [Lakshminarayanan, Rangarajan, Venkatachary], [Yu, Katz], [Spitznagel, Taylor and Turner], [Che, Wang, Zheng, Liu]…

## Slide 17: Using the Extra Symbols
[Liu]
Rule | Source address | Source port | Pro. | 
Rule 1 | 123.25.0.0/16 | <601 | TCP | 
Rule 2 | 13.24.35.0/24 | >1023 | TCP | 
Rule 3 | 16.32.223.14 | 500-600 | UDP | 
Rule 4 | 22.2.3.4 | 1-6 | TCP | 
Rule 5 | 22.2.3.4 | 550 | TCP | 
Rule 6 | 255.2.3.4 | >1023 | ICMP | 
Rule 7 | 13.24.35.0/24 | >1023 | TCP | 
Rule 8 | 168.0.0.0/8 | 1-6 | UDP | 
Rule 9 | 192.132.4.0 | 500-600 | UDP | 
Suppose there is only one field with ranges
R1= [1,6] ; R2 = [1,600] ; R3 = [500,600] ; R4 =[1024,216-1]
Using 4 extra symbols: R1 = 1 ; R2 = 1 ; R3 = 1 ; R4 = 1

## Slide 18: Using the Extra Symbols
[Liu]
Rule | Source address | Source port | Pro. | 
Rule 1 | 123.25.0.0/16 | ********* | TCP | *1**
Rule 2 | 13.24.35.0/24 | ********* | TCP | ***1
Rule 3 | 16.32.223.14 | ********* | UDP | **1*
Rule 4 | 22.2.3.4 | ********* | TCP | 1***
Rule 5 | 22.2.3.4 | 550 | TCP | ****
Rule 6 | 255.2.3.4 | ********* | ICMP | ***1
Rule 7 | 13.24.35.0/24 | ********* | TCP | ***1
Rule 8 | 168.0.0.0/8 | ********* | UDP | 1***
Rule 9 | 192.132.4.0 | ********* | UDP | **1*
Suppose there is only one field with ranges
R1= [1,6] ; R2 = [1,600] ; R3 = [500,600] ; R4 =[1024,216-1]
Using 4 extra symbols: R1 = 1 ; R2 = 1 ; R3 = 1 ; R4 = 1

## Slide 19: Using the Extra Symbols
[Liu]
Rule | Source address | Source port | Pro. | 
Rule 1 | 123.25.0.0/16 | ********* | TCP | *1**
Rule 2 | 13.24.35.0/24 | ********* | TCP | ***1
Rule 3 | 16.32.223.14 | ********* | UDP | **1*
Rule 4 | 22.2.3.4 | ********* | TCP | 1***
Rule 5 | 22.2.3.4 | 550 | TCP | ****
Rule 6 | 255.2.3.4 | ********* | ICMP | ***1
Rule 7 | 13.24.35.0/24 | ********* | TCP | ***1
Rule 8 | 168.0.0.0/8 | ********* | UDP | 1***
Rule 9 | 192.132.4.0 | ********* | UDP | **1*
For each source port x and range Ri compute if xRi . which ranges I
For x=550, we get x  [1,6] ; x  [1,600] ; x  [500,600] ; x  [1024,216-1]
Extra Symbols assigned: 0110
550
0110

## Slide 20: Using the Extra Symbols
[Liu]
Rule | Source address | Source port | Pro. | 
Rule 1 | 123.25.0.0/16 | ********* | TCP | *1**
Rule 2 | 13.24.35.0/24 | ********* | TCP | ***1
Rule 3 | 16.32.223.14 | ********* | UDP | **1*
Rule 4 | 22.2.3.4 | ********* | TCP | 1***
Rule 5 | 22.2.3.4 | 550 | TCP | ****
Rule 6 | 255.2.3.4 | ********* | ICMP | ***1
Rule 7 | 13.24.35.0/24 | ********* | TCP | ***1
Rule 8 | 168.0.0.0/8 | ********* | UDP | 1***
Rule 9 | 192.132.4.0 | ********* | UDP | **1*
For each source port x and range Ri compute if xRi . which ranges I
For x=550, we get x  [1,6] ; x  [1,600] ; x  [500,600] ; x  [1024,216-1]
Extra Symbols assigned: 0110
550
0110
  Pre-computed and stored in a SRAM direct-access array of 216 entries.

## Slide 21: Flow of information
Packet Header
x
SRAM
0
216-1
x
If xRi set the i-th bit to 1,
otherwise 0.
For x=550 we get 0110
Notes: How does it really work? An example

## Slide 22: Problems with the Liu’s scheme
Number of ranges usually exceeds the number of symbols  Cannot encode all the ranges  Degrades to prefix expansion
First solution: encode layers with large penalty first [DRES, 2008]
Our contributions: We observe that n non-intersecting ranges can be encoded using log n bits
Using layering technique in order to achieve (much) better range encoding.
w(r) = (# rules with r) × (prefix-expansion(r) – 1)

## Slide 23: Encoding Ranges
We look at all ranges as intervals over [0,216-1]
0
216-1

## Slide 24: Encoding Ranges - Layering
Partitioning the ranges to layers of disjoint intervals
Each layer gets its own set of symbols
Ranges are encoded starting from (binary) 1
  log(n+1) symbols per n-ranges layer
0
216-1
001
010
011
100
01
10
11
1
1
3 symbols
2 symbols
1 symbol
1 symbol

## Slide 25: Encoding the Ranges
Extra symbols of the layer: range code
Extra symbols of other layers: …
0
216-1
001
010
011
100
01
10
11
1
1
3 symbols
2 symbols
1 symbol
1 symbol
10
Notes: And what if I have only 3 symbols..

## Slide 26: Encoding the SRAM Array
For each layer:
  If x is in any interval  the interval code
  If x is not in the interval  all 0’s
0
216-1
001
010
011
100
01
10
11
1
1
0010010
3 symbols
2 symbols
1 symbol
1 symbol
10
x
x
x
0010010
001

## Slide 27: Towards an Optimal Encoding
Let L1,L2,…,Ln be the sizes of the layers
The number of bits needed to encode all ranges is
It is NP-hard to find an optimal layering given a set of ranges
  By reduction from circular-arc graph coloring
  2-Approximation algorithm based on maximum size k-colorable sets (MSCS)
  Greedy heuristic colors iteratively maximum size independent set (MSIS)

## Slide 28: Coping with “Symbol Budget”
Not all the ranges can be encoded
We use the DRES weight in order to choose the encoded ranges
  Other ranges will be treated with prefix expansion
Given a number of symbols, it is NP hard to find a layering that maximizes the total weight of encoded ranges
  Heuristics take into account the weight MWIS, MWCS

## Slide 29: Choosing the Right Ranges
Pick the layer with maximum gain, and assign it the next symbol.
Layering Stage MSIS, MSCS, MWIS, MWCS
Symbol Allocation Stage Bit Auction algorithm
Within each layer, ranges are sorted by their weight; Lij is the jth range of layer Li
We allocate the symbols one by one.
Encoding Stage
Unencoded range rules are handled w/ Prefix Expansion
Average per-symbol gain for encoding the next k-symbols to layer Li:

## Slide 30: Experimental Results
On real-life rule set
  120 separate rule files from various applications
    Firewalls, ACL-routers, Intrusion Prevention systems
  223K rules
  280 unique ranges
Used as a common benchmark in literature

## Slide 31: Experimental Results
Best Prior Art

## Slide 32: Experimental Results

## Slide 33: Wrap-Up
New solution for range representation
  60% better than prior art
Also deals with:
  Two range fields
  Hot updates of the rules
Future work: IPv6
  32-bits for source-, dest- port fields
  Direct access array in SRAM is infeasible
  Possible solution: use TCAM twice in pipelined manner

## Slide 34: Wrap-Up
Two solutions for major contemporary challenges in TCAM devices
Makes packet classification more efficient (less entries  less power) and robust
Both solutions make use of extra symbols available in TCAM configurations anyway
An Interesting future direction:
  Using TCAMs outside a networking environment

## Slide 35: Thank You