## Slide 1: Efficient Processing of Multi-Connection Compressed Web Traffic
Yaron Koral1
with: Yehuda Afek1 , Anat Bremler-Barr1*
1 Blavatnik School of Computer Sciences Tel-Aviv University, Israel
2 Computer Science Dept. Interdisciplinary Center, Herzliya, Israel
⋆ Supported by European Research Council (ERC) Starting Grant no. 259085

## Slide 2: Compressed Web Traffic
Compressed web traffic increases in popularity

## Slide 3: DPI on Compressed Web Traffic
Thousands concurrent sessions
Uncompressed Traffic
Compressed (Mem. Req. 32KB per Session)
unzip
Space
Time
80%
40%
Contribution:
Improve
DPI

## Slide 4: Background: Compressed HTTP uses GZIP
Two stage algorithm:
  Stage 1: LZ77
    Goal: reduce string presentation size
    Technique: repeated strings compression
  Stage 2: Huffman Coding
    Goal: reduce the symbols code size
    Technique: frequent symbols  fewer bits
Notes: So I’ll start with some background about GZIP
GZIP is combined from two compression algorithms: LZ77 & Huffman coding
LZ77 main goal is to reduce string presentation size by replacing repeated strings in text with pointers
Huffman coding main goal is to reduce coding size by giving frequent symbols, fewer bits representation

## Slide 5: Background: LZ77 Compression
Compress repeated strings
  Looking only 32KB back (window)
Encode repeated strings by {distance,length}
ABCDEFABCD 
ABCDEF
{6,4}
Pointers might be recursive
Notes: For our acceleration algorithm we use the LZ77 characteristics, so I’ll speak more about the LZ77 part.
LZ77 replaces repeated strings from the last 32KB window with a pointer.
The pointer is a distance length pair, while distance indicates the number of bytes to go backward and length indicates the number of bytes to copy from that position.
In this example we see a pointer that replaces the repeated string ABCD.
Another important issue is that Pointers may point to other previous pointers recursively.

## Slide 6: Background: LZ77 Compression
Decompression is cheap
  Copy consecutive bytes to buffer
  Enjoys cache boost due to spatial locality
Compression is expensive
  Maintain locations of previous strings triplets
  Locate (a larger) prior occurrence of current text...
We use this observation later on…

## Slide 7: Current state
Uncompressed
active session buffer
New Packet
unzip

## Slide 8: General Idea: Keep “compressed” buffer
Keep buffers in a “compressed” form
Uncompress “active session” only
Compressed
active session buffer
New Packet
unzip

## Slide 9: 1st attempt – use original data
Problem: pointers may point out-of buffer boundary
Distance between a pointer to its literals may be the entire session!
This usually exceeds 32KB…
… (200,3)…
…(300,5) …abc…
hello… …
(30,000,4)......
Packets
32KB Buffer
INVALID!

## Slide 10: 2nd attempt – re-compress buffer
Upon new packet arrival
  Unzip old buffer
  Unzip packet
  Process data
  Calculate new buffer boundary
  gzip buffer
Pro’s:
  Space efficient: 83% less memory
Con’s:
  Time expansive: 20 times slower!!!
TIME
EXPANSIVE!!

## Slide 11: Our solution: Swap Out of boundary Pointers (SOP)
Buffer PACKING Technique – Light Compression
SOP uses the original GZIP compressed form (as in 1st attempt)
Swap invalid pointer with its referred literals
SOP Compared to 2nd attempt:
  Space 2.6% more memory
  Time: 81.4% faster

## Slide 12: How it works
ello … ...
… abc …
… hello …abc…
hello… …
… (200,3)…
… hello …abc…
hello… …
… (200,3)…
…(300,5) …abc…
hello… …
(30,000,4)......
(30,000,4)…...
(a) Compressed Buffer
(b) Uncompressed Buffer
(c) SOP Buffer

## Slide 13: SOP – Packing Algorithm
Upon new packet arrival
  Unzip old buffer
  Unzip packet
  Process data
  Calculate new buffer boundary
  Swap out-of boundary pointers with literals
New Packet
1.unzip
2.unzip
5.Swap pointer with literals
4.New boundary

## Slide 14: SOP – Time Considerations
Each packet is decompressed several times
  Uncompressed size ~ 4.6KB ( 32/4.6=6.9)
Decompression is cheap! (still…)
Gzip Decompression
time

## Slide 15: SOP-Indexed
Keep indices to chunks within buffer
Decompress only required chunks
SOP-Indexed as compared SOP
  Space loss: 5.8%
  Time gained: 10.3%
New Packet
1.Unzip req. chunks
2.unzip
Chunk
Indices

## Slide 16: DPI of Compressed Traffic
ACCH: Aho-Corasick based algorithm for Compressed HTTP (INFOCOM 2009)
General Idea: skip scanning repeated-strings
Memory Req.: 2-bit status vector per byte
32KB
40KB

## Slide 17: ACCH Algorithm: skip scanning pointer area
Solution: Pack Vector with Data
DPI Scan
Aho-Corasick
ACCH
Skips around 80% of data scans
Status-vector increases space requirement by 25%

## Slide 18: Experimental Results: Packing Methods
 | Avg. Buffer Size | Normalized Packing Time
Naïve (Plain) | 29.9KB | 1
OrigComp (1st attempt) | 4.54KB | -
Recompress (2nd attempt) | 5.04KB | 20.77
SOP | 5.17KB | 3.85
SOP-Indexed | 5.47KB | 3.49

## Slide 19: Experimental Results: DPI +Packing
Unzip entire session.
Avg. Size = 170KB
SOP
1.39, 5.17KB
ACCH 0.36, 37.4KB
SOP+ACCH
0.64, 6.19KB
Naïve
1.1, 29KB

## Slide 20: Conclusion
HTTP compression - gains popularity
High memory requirements  ignored by FWs
SOP reduces space requirement by over 80%.
SOP with ACCH 80% less memory
and 40% faster.